Summary

In this activity, you are asked to design and construct a filter for the purpose improving the water quality of various source waters. We use water quality tests (particularly turbidity) to characterize the performance of your filter design and to assess the opportunities for improvements to the design. Part of the intention of this activity is to provide participants with some experience with how a design on paper may or may not translate well to ease of construction and actual full scale performance

Assignment

Your group will need to develop a filter design on paper before you will be allowed to move to the construction phase of the filter. Once your filter has been constructed, you are expected to test your filter’s performance. The scoring rubric below will provide us a way to measure how well you do versus others.

List of Available Materials

| Material | Cost | Its General Use | Comments about filter expectations/usability |
| --- | --- | --- | --- |
| Coffee filters | $1 (each) |  |  |
| Wax Paper | $3/cm wide |  |  |
| Plastic Wrap | $3/cm wide |  |  |
| Paper Towel | $30/section |  |  |
| Fine Sand | $10/cm |  |  |
| Coarse Sand | $15/cm |  |  |
| Mulch | $20/cm |  |  |
| Activated Carbon | $50/spoon |  |  |
| Pea Gravel | $5/cm |  |  |

Scoring Rubric

| Scoring Category | Poor = 1 | Good = 3 | Excellent = 5 | Score | Weight |
| --- | --- | --- | --- | --- | --- |
| Total Filter Cost | More than $500 | $150 to $500 | Less than $150 |  | 35% |
| Performance (initial design) | More than 30 NTU | 2 to 30 NTU | Less than 2 NTU |  | 10% |
| Adaptability (2nd design) | More than 30 NTU | 2 to 30 NTU | Less than 2 NTU |  | 25% |
| Scalability (cost x 100) | More than $50,000 | $25,000 to $50,000 | Less than $25,000 |  | 15% |
| Speed (Flow) / # of filters | More than 40, less than 15 | 20 to 40 seconds | Btw 15-20 seconds |  | 15% |
| Total |  |  |  |  |  |

| Materials Used | Illustration of Filter Design 1 (label materials and show amounts) | Illustration of Filter Design 2 (label materials and amounts) | Illustration of Filter Design 3 (label materials and amounts) |
| --- | --- | --- | --- |
| Cost Estimate: |  |  |  |
| Time to flow: |  |  |  |